Spring JMX
Spring JMX
Management and Monitoring of Java Applications
[Speaker Notes: Read notes on slide 10 about connecting to TomCat to give people a feel for the process.]

---
Topics in this session
Topics in this session
Introduction to JMX
JMX Architecture
Introducing Spring JMX
Explicitly exporting beans with Spring
Automatically exporting existing MBeans

---
Topics in this session
Introduction to JMX
JMX Architecture
Introducing Spring JMX
Explicitly exporting beans with Spring
Automatically exporting existing MBeans

---
Goals of JMX
Goals of JMX
The Java Management Extensions specification aims to create a standard API for adding management and monitoring to Java applications
Management
  - Changing configuration properties at runtime
Monitoring
  - Reporting cache hit/miss ratios at runtime

---
How JMX Works
How JMX Works
To add this management and monitoring capability JMX instruments application components
JMX introduces the concept of the MBean
  - A Java Bean with a management interface

---
Topics in this session
Introduction to JMX
JMX Architecture
Introducing Spring JMX
Explicitly exporting beans with Spring
Automatically exporting existing MBeans

---
JMX Architecture
JMX Architecture
MBeanServer
MBean
MBean
MBean
JSR-160
Connector
JSR-160
Connector

---
JMX Architecture
An MBean is a standard Java Bean with an additional management interface
  - Attributes
    - where getters and setters define readability and writeability
  - Operations
The management interface can be defined statically with a Java interface or defined dynamically at runtime

---
JMX Architecture
An MBeanServer acts as a broker for communication between
  - Multiple local MBeans
  - Remote clients and MBeans
An MBeanServer maintains a keyed reference to all MBeans registered with it
  - This key is referred to as an ObjectName

---
JMX Architecture
External communication with an MBeanServer is accomplished using a JSR-160 connector
This specification defines a generic API for communicating with an MBeanServer
The only protocol required by the spec is RMI
  - But there are additional protocols including:
    - SOAP
    - Hessian
    - IPC
[Speaker Notes: After this slide is a good time to connect to TomCat via jconsole and give people a look at what MBeans the VM itself, as well as TomCat exposes.]

---
Topics in this session
Introduction to JMX
JMX Architecture
Introducing Spring JMX
Explicitly exporting beans with Spring
Automatically exporting existing MBeans

---
Goals of Spring JMX
Goals of Spring JMX
Using the raw JMX API is difficult and complex
The goal of Spring's JMX support is to simplify the use of JMX while hiding the complexity of the API

---
Goals of Spring JMX
Exposing existing Spring beans as MBeans
  - Transparently without changing any Java code
  - Declaratively using Spring bean definitions
Configuring JMX infrastructure
  - Declaratively using FactoryBeans
Consuming JMX managed beans
  - Transparently using a proxy-based mechanism

---
Topics in this session
Introduction to JMX
JMX Architecture
Introducing Spring JMX
Explicitly exporting beans with Spring
Automatically exporting existing MBeans

---
Creating an MBeanServer
Creating an MBeanServer
To create an MBeanServer declaratively, define a bean
<bean id="mBeanServer"
class="org.springframework.jmx.support.
        MBeanServerFactoryBean">
<property name="locateExistingServerIfPossible" value="true"/>
</bean>

---
Spring's MBeanExporter
Spring's MBeanExporter
Transparently expose an existing POJO bean to the MBeanServer
  - No need to write the registration code
By default avoids the need to create an explicit management interface or create an ObjectName instance
  - Uses reflection to manage all properties and methods
  - Uses map key as the ObjectName

---
Exporting a bean as an MBean
Exporting a bean as an MBean
Start with an existing POJO bean
Use the MBeanExporter to export it
<bean id="messageService" class="MessageService"/>
<bean class="org.springframework.jmx.export.MBeanExporter">
<property name="beans">
   <util:map>
       <entry key="service:name=messageService"
        value-ref="messageService"/>
   </util:map>
</property>
</bean>
[Speaker Notes: DEMO: a demo for this can be found in the cookbook section of the jmx-1 module]

---
Controlling MBean Details
Controlling MBean Details
In many cases the default strategies for creating the management interface and setting the ObjectName are not sufficient
The MBeanExporter allows alternative strategies to be injected
  - ObjectNamingStrategy
  - MBeanInfoAssembler

---
ObjectNamingStrategy
ObjectNamingStrategy
ObjectNames are controlled by implementations of the ObjectNamingStrategy interface
Three included implementations
  - KeyNamingStrategy
    - Default implementation
    - Uses the key passed to the MBeanExporter by default
    - Can be configured to look in a properties file
  - IdentityNamingStrategy
    - Generates an ObjectName dynamically based on the JVM identity of a bean
  - MetadataNamingStrategy
    - Reads an ObjectName from source-level metadata

---
ObjectNamingStrategy
<bean class="org.springframework.jmx.export.MBeanExporter">
<property name="beans">
   <util:map>
       <entry key="not.important"
        value-ref="messageService"/>
   </util:map>
</property>
<property name="namingStrategy">
   <bean class="org.springframework.jmx.export.naming.
        IdentityNamingStrategy"/>
</property>
</bean>

---
MBeanInfoAssembler
MBeanInfoAssembler
Management interfaces are controlled by implementaions of the MBeanInfoAssembler interface
  - Builds on the JMX standard ModelMBean infrastructure
  - Allows for the full feature set of JMX to be exposed
  - Easily extensible for your own requirements

---
MBeanInfoAssembler
Four included implementations
  - SimpleReflectiveMBeanInfoAssembler
    - Default implementation
    - Exposes all public properties and methods
  - MethodNameBasedMBeanInfoAssembler
    - Supports declarative selection of methods in a Spring configuration file
    - Extremely easy to configure
    - Allows per instance configuration

---
MBeanInfoAssembler
  - InterfaceBasedMBeanInfoAssembler
    - Supports management interface definition using Java interfaces
    - Extends the Standard MBean interface semantics
      - Use multiple interfaces per bean
      - Beans do not need to implement the management interface directly
  - MetadataMBeanInfoAssembler
    - Define management interfaces using source-level metadata
      - JDK 5.0 Annotations
    - Supports autodetection
      - Any bean marked with the @ManagedResource annotation will be automatically registered with an MBeanServer

---
MBeanInfoAssembler
<bean class="org.springframework.jmx.export.MBeanExporter">
…
<property name="assembler">
   <bean class="org.springframework.jmx.export.assembler.
        InterfaceBasedMBeanInfoAssembler">
       <property name="interfaceMappings">
        <util:map>
        <entry key="service:name=messageService"
        value="infoassembler.MessageCapable" />
        </util:map>
       </property>
   </bean>
</property>
</bean>
[Speaker Notes: DEMO: uses annotation-app from the cookbook section in the jmx-1 module]

---
Topics in this session
Introduction to JMX
JMX Architecture
Introducing Spring JMX
Explicitly exporting beans with Spring
Automatically exporting existing MBeans

---
Automatically exporting
pre-existing MBeans
Some beans are Mbeans themselves
  - ActiveMQ ConnectionFactory
  - Hibernate StatisticsService
Spring can easily autodetect those and export them for you
<context:mbean-export/>
<bean id="connectionFactory"
        class="org.apache.activemq.ActiveMQConnectionFactory">
        <property name="brokerURL" value="..."/>
</bean>

---
Summary
Spring JMX allows you to easily export
Spring-managed beans to a JMX MbeanServer
  - Simple value-add now that your beans are managed
Use MbeanInfoAssembler to customize the management interface
Using <context:mbean-export> to automatically export pre-existing MBeans

---
LAB
LAB
Adding Management and Monitoring
with Spring JMX